## Slide 1
A
LVLH inspection geometry and candidate views
x₀ initial state
radial x
along-track y
cross-track z
Station-primitive safety envelope
signed clearance ≥ 0
● covered sample
● not yet covered
B
Camera visibility and dwell accumulation
camera aperture
ρₘᵢₙ ≤ ‖pᵢ − rₖ‖ ≤ ρₘₐₓ
boresight b(qₖ)
FOV half-angle αₘₐₓ
nᵢ
incidence θᵢ ≤ θₘₐₓ
LOS = 1
visible
LOS = 0
occluded
t(k)
t(k+1)
t(k+m)
⋯
⋯
if visible: τᵢ,ₖ₊₁=τᵢ,ₖ+Δt
otherwise: τᵢ,ₖ₊₁=τᵢ,ₖ
yᵢ,ₖ=𝟙[τᵢ,ₖ≥τₘᵢₙ]
Visible samples accumulate target-indexed dwell; invisible samples leave τ(i) unchanged.
C
Directed graph of HCW-feasible SOOAs
a₁
a₂
a₃
a₄
a₅
a₆
a₇
a₈
a₉
a₁₀
η(a,b) = 0 → removed
SOOA node aⱼ stores
visible set Γⱼ
control effort Δvⱼ
clearance dₘᵢₙ,ⱼ
passive margin ρⱼ
Edge ηₐᵦ=1 with cost ℓₐᵦ:
HCW rollout passes terminal, input, speed, clearance, and passive-drift tests.
D
Dynamics-aware planning rejects unsafe actions
Geometry-only ordering
coverage-rich selection, checked afterward
Dynamics-aware SOOA planning
feasibility audited before an arc contributes coverage
×
x₀
high ΔC
✕ clearance dₘᵢₙ < 0
✕ peak input > uₘₐₓ
Rejected after rollout
x₀
C ≥ 98%
✓ ZOH input/speed bounds
✓ clearance dₘᵢₙ ≥ 0
✓ v(T)=0; passive margin ≥ 0
OrbInspect selects finite-duration SOOAs that are observable, HCW-feasible, input/speed bounded, clearance-safe, terminally stabilized, and passively audited.
Notes: [Sources]
- Local manuscript: /Users/supocoral/Github/OrbInspect/OrbInspectLatex/main.tex, especially the visibility/dwell model (lines 243–260), dynamic feasibility and cost (lines 264–287), SOOA definition and passive audit (lines 289–319), and finite graph (lines 344–372, 465–501).
- Local implementation: src/orbinspect_safety/orbinspect_safety/keepout_zones.py (station-primitive safety envelope rather than an ellipsoid).
- All visual elements are native editable PowerPoint shapes; no external image assets are embedded.