## Slide 1
A
LVLH inspection geometry and candidate views
x₀ initial state
radial x
along-track y
cross-track z
Station-primitive safety envelope
signed clearance ≥ 0
● covered sample
● not yet covered
B
Camera-valid mask at a prescribed observation
camera aperture
ρₘᵢₙ ≤ ‖pᵢ − rₖ‖ ≤ ρₘₐₓ
boresight b(qₖ)
FOV half-angle αₘₐₓ
nᵢ
incidence θᵢ ≤ θₘₐₓ
LOS = 1
visible
LOS = 0
occluded
pose j
tests
Gⱼ
⋯
⋯
Gⱼ={i: all tests pass}
select j: m⁺=m∨Gⱼ
exposure prescribed
A stabilized pose credits fixed mask Gⱼ; dwell/exposure time is not integrated.
C
Observation nodes and source-dependent SOOA edges
v₁
v₂
v₃
v₄
v₅
v₆
v₇
v₈
v₉
v₁₀
audit fails → edge removed
Observation node vⱼ stores
terminal pose
r̄ⱼ, q̄ⱼ
visible mask Gⱼ
SOOA edge aᵢⱼ stores:
trajectory + controls
cost + sampled audits
(input, speed, clearance,
terminal, passive drift)
D
Dynamics-aware planning rejects unsafe actions
Geometry-only ordering
coverage-rich selection, checked afterward
Dynamics-aware SOOA planning
feasibility audited before an arc contributes coverage
×
x₀
high ΔC
✕ clearance dₘᵢₙ < 0
✕ peak input > uₘₐₓ
Rejected after rollout
x₀
C ≥ 98%
✓ held-input RK4 rollout
✓ sampled bounds + clearance
✓ terminal + passive audits
OrbInspect links camera-valid observation nodes through finite-duration HCW SOOA edges that pass all enabled sampled audits.
Notes: [Sources]
- Local manuscript: /Users/supocoral/Github/OrbInspect/OrbInspectLatex/main.tex, especially the visibility/dwell model (lines 243–260), dynamic feasibility and cost (lines 264–287), SOOA definition and passive audit (lines 289–319), and finite graph (lines 344–372, 465–501).
- Local implementation: src/orbinspect_safety/orbinspect_safety/keepout_zones.py (station-primitive safety envelope rather than an ellipsoid).
- All visual elements are native editable PowerPoint shapes; no external image assets are embedded.